## Slide 1: CPSC3300: Computer Systems Organization
Lecture 8½ – Karnaugh Maps and Review / Outline of Topics for Exam 1

## Slide 2: Logic Functions in Two-Level Representation
SoP can be used to determine the logic functions of variables
Example: identify the function for Cout
  Given 3 variables A, B, Cin, #literals?
    6 literals: A, B, Cin, , ,
  What are the minterms with three variables?
  How to determine the function?
input |  |  | output
A | B | Cin | Cout
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Minterm for each row, as if its value is 1
  1. 2. 3.
  4. 5. 6.
  7. 8.
Two level representation procedure
  Locate the entries with 1 and represent them with minterms
  Add the minterms

## Slide 3: Simplification of Boolean Logic Functions
The sum-of-products representation is usually not the most efficient function to implement in a circuit
  Using a simplified function reduces the gates needed
Example:
  Simplifies to:
Various methods exist to simplify Boolean functions written using two-level representation (sum-of-products when using minterms)
  Karnaugh maps (Karnaugh–Veitch maps)
  Quine–McCluskey algorithm (method of prime implicants)
  ESPRESSO algorithm

## Slide 4: Karnaugh Maps
Results from the Boolean function (outputs) are arranged onto a 2-dimensional grid with each cell position representing a combination of input conditions (minterm)
input |  |  | output
A | B | Cin | Cout
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
 |  | AB |  |  | 
 |  | 00 | 01 | 11 | 10
Cin | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 1 | 1

## Slide 5: Karnaugh Maps
To form the simplified expression, using the Karnaugh map group together adjacent cells with a value of 1 in a rectangle of 2x width and 2y height maximizing x and y without including any cells with a value of 0
  Repeat until all cells with 1 are in such a group, any isolated cells with 1 are grouped in a 1x1 rectangle
 |  | AB |  |  | 
 |  | 00 | 01 | 11 | 10
Cin | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 1 | 1
Values for A match: 1
Values for B match: 1
Values for Cin don’t match
Values for A match: 1
Values for B don’t match
Values for Cin match: 1
Values for A don’t match
Values for B match: 1
Values for Cin match: 1

## Slide 6: Karnaugh Maps
The resulting simplified expression will be the sum of each of the groups.
  Each group corresponds to a product of all values of an input variable with a value of 1 corresponding to all grouped cells and the negated value of an input variable with a value of 0 corresponding to all grouped cells
 |  | AB |  |  | 
 |  | 00 | 01 | 11 | 10
Cin | 0 | 1 | 1 | 0 | 0
 | 1 | 0 | 0 | 1 | 1
Values for A match: 0
Values for B don’t match
Values for Cin match: 0
Values for A match: 1
Values for B don’t match
Values for Cin match: 1

## Slide 7: Administrivia
Exam 1 on Wednesday February 12
  In class, same room and time
  Time allowed: 75 minutes
  No notes, no calculator, no textbook
  You may bring a half letter size (approx. 8.5” x 5.5”) reference sheet with handwritten notes on one side

## Slide 8: Exam 1
Format
  Written exam, 11 - 13 questions (100 points) and 2 extra credit questions (+10 points)
  Response types include short-answer/fill-in-the-blank (including selection), mathematical questions (formula / calculation, numbers used will be simple) and a few longer answer questions (truth tables, logic gate circuits, etc.)
Chapters covered:
  Chapter 1: Technology, improvements in computer hardware, performance and benchmarking (Lectures 1 – 4)
  Appendix B: Combinational logic, adders, sequential logic, finite state machines and counters (Lectures 5 – 8)
  Not in textbook (limited to extra credit): Karnaugh maps

## Slide 9: Outline of Topics
Lecture 1 – Introduction
  Progress in computer technology, Moore’s law, Dennard Scaling
  Types of computers
  Hardware vs. software
  High level language vs assembly vs. machine language
Lecture 2 – Technology, Performance and Power
  Orders of magnitude (giga / nano, etc.)
  Response time vs. throughput
  Relative performance / speedup
  Measuring execution time

## Slide 10: Outline of Topics
Lecture 3 – Technology, Performance and Power II
  Elapsed time vs. CPU time
  CPU clock cycle
  CPU Performance equation (instruction count, cycles per instruction, seconds per cycle), possible influencing factors
  Amdahl’s law and overall speedup
  Comparison of performance using clock rate, CPI and IC
Lecture 4 – Benchmarking
  Power usage (capacitive load, voltage, frequency)
  Methods (real programs / modified apps / kernels / synthetic benchmarks (i.e. whetstone), benchmarking suites
  Comparing benchmarks using arithmetic mean vs. normalized geometric mean

## Slide 11: Outline of Topics
Lecture 5 – Combinational Logic
  Logic gates and functions (AND, OR, NOT, etc.)
  Boolean algebra (laws of, DeMorgan’s Theorem)
  Truth tables, logic functions and two-level representation (sum of products)
  Logic gate circuit diagrams
Lecture 6 – Adders
  Multiplexers
  Half adder and full adder
  Carry-lookahead adders, using “generate” and “propagate” to calculate carry values
  Performance of a ripple adder vs. a carry-lookahead adder

## Slide 12: Outline of Topics
Lecture 7 – Sequential Logic
  Arithmetic Logic Unit
  Circuits with a state (“memory”), memory cells, feedback circuits
  S-R Latch, D Latch, Edge-triggered D Flip-Flop
  Latches vs. flip-flops
  Register file
Lecture 8 – Counters and Finite State Machines
  State machine model: inputs, states, transition (to another state) and output
  State diagrams and state transition tables
  Circuit design of state machines (using D flip-flops for state bits)
  Counters

## Slide 13: Outline of Topics
Lecture 8½ – Karnaugh Maps and Review (not in the textbook)
  Simplification of sum of products Boolean function
  Converting a truth table to a Karnaugh map
  Grouping cells with a ‘1’ value to form a product term
  Simplified function is the sum of the product terms for each group